## Slide 1
Blood Pressure Estimation Using a Smartphone Camera
Results
Students: Dan Ben David & Topaz Aharon
Supervisor: Yair Moshe
Signal and Image Processing Lab
Blood Pressure
The pressure exerted upon the walls of blood vessels
Expressed using systolic / diastolic pressure
High blood pressure – “the silent killer”
Low blood pressure has also its negative effects
Continuous monitoring of blood pressure is important in many medical conditions
Goal
Estimate blood pressure using a smartphone camera
Challenges
Very noisy signals
Lack of tagged data
Should meet measurement accuracy standards
Accuracy was measured as a success if the loss between the prediction and the true BP was less then 5 mmHg
Comparison to naive algorithm (average BP as an estimator)
We have achieved better results than the naive way
To meet medical standards, we should obtain
  Accuracy over 95%
  Loss < 5 mmHg
We believe that acquiring a larger labeled database from smartphones will significantly improve results
PPG Signal
Obtained by illuminating the skin and measuring absorption
Oximeter – infrared light and red light, transmission
Data Collection
Parallel sampling using a blood pressure monitor and a smartphone camera
Each sample is approximately 40sec
15 different people, 200 samples in total
PPG from Smartphone
Mimic an oximeter using the camera and the flash light of the smartphone
Transfer Learning
Due to our small dataset, we also tried to perform transfer learning with only one fully-connected layer
Smartphone – white light, reflective
Extract relevant frequencies from the acquired video
Find threshold value for the red channel
Remove noisy frames
Create a PPG signal
Pulse
frames
Raw
Baseline
For every frame: 𝑅[𝑖]
If: (0.25𝑁_𝑖<𝑅[𝑖]<𝑁_𝑖 ) 𝑃𝑃𝐺[𝑖] = (𝑀𝑎𝑥 ⁡(𝑅)−𝑅[𝑖]) / (𝑀𝑎𝑥(𝑅)−𝑀𝑖𝑛(𝑅) )
Else remove frame
Remove baseline
Time[Sec]
Pulse []
Time[Sec]
Frequency[Hz]
Transform to a spectrogram
conv layers
fully-connected layers
MIMIC-II
Smartphone
Time[Sec]
Time[Sec]
Frequency[Hz]
Frequency[Hz]
conv layers
fully-connected layer
Transfer learning
accuracy: 45.0
loss: 9.66
Naive
accuracy: 0.0
loss: 18.84
System Scheme
Offline
Video to PPG
Video from smartphone
Preprocessing
PPG with
BP label
Training
Model
Transfer Learning
Smartphone PPG with BP label
PPG signal
Preprocessing
Blood Pressure Estimation
Refined Model
Systolic/Diastolic values
Online
Preprocessing
Convert video to PPG
Upsample from 30Hz to 125Hz
Cut middle 30 sec
MIMIC-II is a database with physiologic signals from tens of thousands of Intensive Care Unit (ICU) patients
For over 1500 patients, the database contains PPG signals with corresponding BP values
Previous project created a BP estimation network using MIMIC-II
  Inspired by AlexNet architecture
We used transfer learning on this network to train the model on our dataset
60% training 20% validation, 20% test